## Slide 1: Tanacious
AI SYNERGY HACKATHON 2026 · CASE 05
Seeing the 4 PM spike in buildings that only send a bill
A campus energy engine that rebuilds 15-minute load from monthly bills
Notes: Open with the line: you can’t optimise what you can’t measure. We’re Tanacious, and we tackle Case 05, the 4 PM spike.

## Slide 2: You can’t cut a peak you can’t see
01 · PROBLEM STATEMENT
The 4–8 PM spike
Weekday demand jumps just as rooftop solar fades.
The missing meter
Some buildings report every 15 minutes. Others send one bill a month.
The flat split fails
Spreading a bill evenly hides the spike in the exact hours that matter.
Notes: Demand peaks 4–8 PM on weekdays while solar drops. Facilities can’t shift load they can’t see, and half the campus only sends a monthly bill. An even split of that bill wipes out the spike. They also need to know flexible load, like hostel cooling, from critical load, like labs, before touching anything.

## Slide 3: Three steps from bill to 15-minute curve
02 · PROPOSED SOLUTION
1
Learn the shape
A Random Forest learns from schedule, weekends, breaks and heat. No clock time.
2
Match the bill
Each month adds up to its utility bill, within 0.01 kWh.
3
Keep real readings
Meter data comes back unchanged. Only the gaps are filled.
Notes: The model trains on every real 15-minute reading: smart meters plus temporary pilot meters. We left clock time out on purpose, so it follows each building type’s own routine instead of copying the metered buildings’ timing. The bill sets the absolute level. Real readings change by 0 kWh, and our tests check that.

## Slide 4: People bring the routine, AI learns the response
03 · PROOF OF SYNERGY · WHAT EACH SIDE BRINGS
Human
Building schedules, weekend and vacation habits, the academic calendar, the bill.
Alone: 24% error. Rough guesses miss the weather and the real timing.
AI
Learns from every 15-minute reading how load bends with heat, weekends and breaks.
Alone: 16% error. It copies the metered buildings’ timing onto every other type.
Human + AI
People set the routine and the total. AI learns how the load responds.
Together: 9.7% error, better than either alone on every building tested.
Notes: The split of work. The facilities team knows things no meter records: each building type’s rough daily routine, how busy it stays at weekends and in vacations, the academic calendar, and the monthly bill. The AI, a Random Forest, learns from every real 15-minute reading how load actually responds to heat, weekends and breaks. Alone, the human estimates are rough and ignore weather: 24% error on real meters. Alone, the AI has nothing to tell building types apart except clock time, so it copies the metered buildings’ timing onto unmetered ones: 16%. Together: 9.7%. Errors are mean WAPE on the real campus with 30% of days hidden.

## Slide 5: Human + AI beat both alone on 12 of 12 buildings
03 · PROOF OF SYNERGY · (HUMAN + AI) ≥ (HUMAN, AI)
Test (mean error) | Human only | AI only | Human + AI
Synthetic campus, 5 buildings | 14.8% | 20.6% | 7.3%
Real campus, 30% of days hidden | 24.2% | 16.3% | 9.7%
Real campus, no meter at all | 24.7% | 17.2% | 12.6%
Real campus, 4–8 PM energy | 13.6% | 6.2% | 2.5%
Human only: the facilities team’s schedule estimates, scaled to the bill. AI only: the same Random Forest on weather, calendar and clock time, with no human inputs.
WAPE on hidden readings, lower is better · Real campus: 7 meters, Building Data Genome Project 2, CC BY-SA 4.0
Notes: This is the synergy proof, measured rather than claimed. Same buildings, same hidden readings, same bill reconciliation; only the shape changes. Human only uses the facilities schedules scaled to each bill. AI only is the same Random Forest given weather, calendar and clock time but none of the human knowledge. Human plus AI is Tanacious. It beats both on all 5 synthetic buildings and all 7 real meters with 30% of days hidden, 12 of 12. With a building fully unmetered it still wins on 6 of 7; the exception is the real library, where the human estimate alone did slightly better, 28.6 versus 32.5 percent. On the 4–8 PM window that matters most, error falls to 2.5 percent, against 6.2 for AI alone and 13.6 for human alone.

## Slide 6: How the AI is put to work
04 · AI UTILISATION · MODEL, RESPONSE, OUTCOME
1
Model
A Random Forest: 100 trees, 14 inputs. Runs on a laptop CPU.
2
Response
Per building: a 15-minute curve, its tested accuracy and a likely range.
3
Outcome
Who drives the 4–8 PM peak. Pre-cool 25% earlier: peak −4.6%.
Notes: How the AI is used. The model is a Random Forest with 100 trees and 14 inputs: weekend, break, temperature and its 3-hour mean, cooling degrees, and the human schedule features. It needs no GPU and no cloud. Its response, for every bill-only building, is a 15-minute load curve that adds up to the bill, the accuracy it scored in testing, and a likely range built from those tested errors. The outcome for facilities: they can see which building types drive the 4–8 PM peak, and try what-ifs. Moving 25% of flexible cooling from 4–8 PM to 10 AM–4 PM cuts the campus peak by 4.6% in an average month. The next slides are the benchmarks.

## Slide 7: 13 of 14
04 · BENCHMARK · TESTED ON REAL CAMPUS METERS
real-meter tests where we beat the flat bill split
7 buildings on a US university campus, 2017 · Building Data Genome Project 2
Notes: This is the slide to land. We didn’t only test on our own synthetic data. We took a peer-reviewed public dataset of real campus meters, hid real readings, rebuilt them and compared. The model won 13 of 14 tests. The one loss was a nearly flat lab, where an even split already works.

## Slide 8: Error drops by half on classrooms and the library
04 · BENCHMARK · REAL DATA, 30% OF DAYS HIDDEN
Meter | Tanacious error | Flat bill split
Classroom Nilda | 9.4% | 21.2%
Classroom Long | 13.4% | 26.6%
Lab Andre | 4.5% | 8.2%
Lab Theodore (nearly flat) | 3.9% | 3.5%
Dormitory Helen | 9.2% | 13.3%
Dormitory Winifred | 5.9% | 7.8%
Library Bart | 21.4% | 40.1%
WAPE on hidden hours, lower is better · Building Data Genome Project 2, CC BY-SA 4.0
Notes: Each row is a real meter. We hid 30% of its days and rebuilt them from the rest plus the monthly totals. Classrooms and the library roughly halve the error. The one loss is Theodore, a nearly flat lab, where an even split is already close. Hiding a two-week block in September gave the same picture, 13 of 14 overall.

## Slide 9: The peak lands in the right place
04 · OUTCOMES · SYNTHETIC CAMPUS, HIDDEN TRUTH KNOWN
0.2–4.6%
error on 4–8 PM energy, per building
4 of 5
buildings with the peak hour exactly right
7.5%
error with 25% of days metered (flat split: 28.6%)
Notes: On synthetic data we know the hidden truth, so we can score everything. The 4–8 PM energy error is 0.2 to 4.6 percent per building, and the peak hour is exactly right for four of five buildings. A few metered days help a lot: the Academic block goes from 11.3 to 7.5 percent with a quarter of days metered, while the flat split stays near 28.

## Slide 10: What’s new in our approach
05 · NOVELTY
Locked to the bill
Each month matches its bill within 0.01 kWh. Real readings stay unchanged.
Human knowledge as input
No clock time, so it carries over to building types with no meter.
Built to be checked
Upload meters, hide readings, rebuild and score them in the dashboard.
No new hardware
Monthly bills plus a few weeks of temporary pilot meters.
Notes: Four things set this apart. One: it is locked to the bill. Every rebuilt month adds up to its utility bill within 0.01 kWh, and real readings come back unchanged, so the output never contradicts what the campus already pays for. Two: human knowledge goes in as model input, not as a manual override. We left clock time out on purpose, which is why it carries over to building types that have no meter at all. Three: it is built to be checked. Any campus can upload its own meters, hide readings and see how close we get, against the flat split. Four: no new hardware. Monthly bills plus a few weeks of temporary pilot meters are enough.

## Slide 11: What it can’t do yet, and what’s next
05 · LIMITS AND WHAT’S NEXT
Today
Synthetic scores are optimistic, so we tested on real meters too
It doesn’t know another campus’s holidays
Simulate is a planning sketch, not a controls system
Next
Read each campus’s own calendar
Learn building schedules from data
Real billing periods, daylight saving, access control
Notes: Say these before the judges do. Our schedules were designed alongside the synthetic generator, which is why the real-data test matters. On the real campus the model didn’t know their holidays, and it expected the library to peak in the evening when it peaks at midday. Simulate assumes buildings can store cooling for a few hours. It rebuilds past months and is not a forecaster.

## Slide 12: One dashboard, four questions
06 · PROTOTYPE DEMONSTRATION
Campus overview
Who drives the 4–8 PM peak?
Building
One curve, its tested accuracy and likely range
Simulate
Pre-cool 25% earlier: campus peak −4.6% a month
Test on your data
Upload meters, hide readings, check us
Notes: Demo order. 1: Campus overview, the stacked peak by building type. 2: Building, a bill-only hostel with its range. 3: Simulate, move 25% of flexible cooling from 4–8 PM to 10 AM–4 PM; peak drops 4.6% in an average month and no month gets worse. 4: Test on your data, load the real campus file, drag to hide a date range, rebuild and compare with the real readings and the flat split. Line: any campus can check us before trusting us.

## Slide 13: Monthly bills in. A 15-minute campus picture out. It matches the bill, never alters a real reading, and you can check it on your own data.
Tanacious · thank you
Notes: Closing line: that’s what a facilities team needs before it touches the 4 PM spike. Then open for questions.